## Slide 1: CSCI 45 – Memory Management
Professor Charles Francis Xavier

## Slide 2: Agenda
Group Projects
Seg Faulting
Memory Management
HW6

## Slide 3: Group Projects
Run through the Baking Pi tutorial in your groups
Document every phase with photos
Your Iron Chef Challenge is:
  Use bare metal assembly.
  You have to use NEON in a meaningful way.
  Make something neat.
Due in two weeks from today.
Get me your proposal by next class

## Slide 4: Seg Faulting
Consider the following code:
  LDR R0, =0x00011000
  LDR R1, [R0]
This reads 32 bits (one word) from the memory address 0x00011000
If you try running this in UNIX, you will seg fault.
Why?

## Slide 5: Seg Faulting
Consider the following code:
  LDR R0, =0x00010000
  LDR R1, [R0]
This reads 32 bits (one word) from the memory address 0x00010000
This will work fine.
Why?

## Slide 6: Seg Faulting
A seg fault takes place when your program tries to access memory that someone has decided you should not be able to access.
The system’s memory management unit detects the fault.:
  “You don’t have access!”

## Slide 7: Interrupt Table
The MMU triggers an interrupt on the operating system, which is just an address of a function.
  This function is part of the OS.
When an OS loads, it tells the CPU the address of all of its interrupt handlers
  For example: “If a segmentation fault occurs, call the function at 0x40001000”.
  Or: “If a network packet arrives, call the function at 0x40002000”.

## Slide 8: Interrupts
So interrupts are a really neat way of being able to handle rare events without having to constantly poll for them.
Polling:
  “Hey, Ms. Network Card! Got any data?”
  “Hey, Mr. Keyboard! Got any data?”
  Etc.
With interrupts, whenever they have some new data, they tell the OS.

## Slide 9: Interrupts
Each device basically gets its own interrupt request line (IRQ).
So when you hit a key on the keyboard, that might trigger interrupt request #16, and the OS will pause your program, call the function to handle it, read the keystroke, and then put the key into the standard input.
cat /proc/interrupts to see the list of interrupts set up in Linux.

## Slide 10: Interrupts
In olde systems, you could have conflicts if two devices both wanted to use the same interrupt request line.
In modern systems, devices can share request lines just fine, so this is no longer a problem users have to worry about.
If multiple devices trigger at the same time, the one with the highest priority executes first.

## Slide 11: Seg Faulting
So when your a.out program tries to access memory that the OS has declared out of bounds for whatever reason, the OS will trigger the seg fault function the OS has set up.
The OS then can choose what to do with your program. Most of the time, it’ll just kill it, and print “SEGMENTATION FAULT” to the screen.

## Slide 12: Seg Faulting
However, if you have enabled core dumping (“unlimit coredumpsize”), then the OS’s seg fault function will also save the current state of your program, including what line of code it was executing, to a core file.
A core file is a snapshot of all of your program’s memory at the time of death.
You can then GDB it.

## Slide 13: MMU
So how do we know when something is out of bounds?
This is what a part of the system called the Memory Management Unit is for.
Whenever a program tries accessing a spot in memory, it has to pass through the MMU first.
If your access is not allowed, SEG FAULT.

## Slide 15: MMU
The MMU does more than that, though.
It can give each program its own address space, which means every program can think that it is loaded at memory address 0 or whatever, but in reality, it might be in some totally different part of RAM.
Your program operates in a virtual memory space, which the MMU translates to a physical memory location.

## Slide 16: MMU
Suppose your program thinks it starts at memory address 0x0, but it is really loaded at memory address 0x10000000.
When your program says to load from memory address 0xF, the MMU will:
  First check to see if that’s a legit access
    If not, SEG FAULT
  Second, translate it into a physical address (RAM location 0x1000000F), and do the load.

## Slide 17: Translation Lookaside Buffer
As you can imagine, it can be hard to map between all these different programs (which might even be running under different OSes on the same machine) and their virtual and physical memory locations.
So the “TLB” is a cache specifically to keep track of these translations.

## Slide 18: Translation Lookaside Buffer
“Each TLB entry contains a virtual address, page size, physical address, and a set of memory properties that include the memory type and access permissions. Each entry is marked as being associated with a particular Application Space ID (ASID), or as global for all application spaces. The TLB entry also contains a field to store the Virtual Machine Identifier (VMID) that brought in the entry” -Source

## Slide 19: MMU
This allows you to protect the OS from unwelcome modifications.
A program is limited to its own segment space, so the only memory that it can access are the memory locations mapped in by the OS.
For example, the OS might want to share its ethernet buffer with your program.

## Slide 20: Memory Mapping
So when the OS creates your program, loading the object code into the CODE segment of your program, initializing the BSS, etc., it can also map into a certain address in memory (often above the stack) the ethernet buffer.
So your program could read directly from it for whatever reason.

## Slide 21: Memory Mapping
But the point is, normal user programs only get access to what the OS allows it access to.
Any attempts to go outside your allowed map are detected and killed by the MMU.
The mmap() syscall can be used to request that the OS map in some memory for you, for example the GPIO memory.
But... this takes root access usually.

## Slide 22: Memory Mapping
One of the nice things about doing bare metal assembly is that the MMU is disabled when the CPU first boots. (This is how the OS can set up everything to begin with.)
So you can just read and write to the GPIO’s memory directly without seg faulting or using mmap.

## Slide 23: Memory Maps
At the end of the day, every program , user, OS, bare metal assembly, whatever, is going to have a “memory map” that it can play with.
This is not just the CODE, BSS, STACK, and HEAP, but also special places in memory that do special things.
Like turning on GPIO pins, or playing music, or writing to the GPU, etc.

## Slide 24: Memory Maps
Every system you work on will put things in different places in memory.
  (And not all peripherals get memory mapped…)
The first thing you do when coding ASM on a new system is to find the memory addresses of the peripherals you want to write to, and write them down.
Example memory map.
And then look up how to use each thing.

## Slide 25: Group Projects
Now that you understand memory maps, you can meet in your groups to look up the memory map for the RPI2 and figure out what you can do for your bare metal group project.
Meet in your groups.