## Slide 1: CSCI 45 – Lecture 3 Assembly Programmin’
Professor Kerney

## Slide 2: Agenda
Review Homework 1.5
Update your RPis
Assembly Programming

## Slide 3: Review Homework 1.5
Grab a copy of each other’s homework.
See if you can decipher their encoding system for writing down commands.
See if you can get their original programs back from 1s and 0s.

## Slide 4: Instruction Decoding
This process you just did, of looking at 1s and 0s, is a crucial step inside of every CPU, called instruction decode.
Basically, given some crazy pattern of bits, what command should we execute?
  How exactly it executes a command we’ll learn later
  This is just the step to figure out what command to do

## Slide 5: Instruction size
In the early days of computing, instructions could take a variable number of bits.
This was nice when a CPU processed one command at a time, since you could add a 4 bit number and a 300 bit number together very simply in assembly.
However, as CPUs got more complicated, we wanted to be able to read ahead and look at upcoming instructions.

## Slide 6: Instruction SIZE
On an IBM Mainframe, there was no limit to instruction sizes (up to the system’s memory, I guess)
On x86 systems, you can have commands that range between one byte and 15 bytes (120 bits).
On ARM, most commands are exactly 32 bits (4 bytes), with one exception.
  (And that exception was a mistake, remedied in ARM64.)

## Slide 7: RISC Computer Architectures
Key Concept Alert!
RISC is a design philosophy that a CPU should have a reduced set of instructions (as few as possible) so that the hardware can be simple, cheap and fast.
Ideally, each command will be exactly 32 or 64 bits
  (Depending on if you’re on a 32-bit system or a 64-bit one.)
Ideally, each command runs in exactly one cycle

## Slide 8: CISC Computer Architectures
CISC systems take the opposite approach: allow more complicated instructions to be added to the CPU, since it’s much faster to run a command like cosines or divides in hardware.
  RISC systems have to implement anything complicated in software
One downside is that instruction decoding is complicated
If I told you to “go to the command 10 instructions down the line” you would have to decode all 10 of them to get there.
  A RISC system would just jump 10 x 4 bytes ahead in memory.

## Slide 9: RISC vs CISC
Even though it seems like CISC would have the advantage, when all the math was worked out, RISC was found to be the superior approach.
This is why most CPUs these days are RISC.
Even x86 systems are RISC now, on the inside. They have a very complicated front end that converts the CISC ISA to RISC. (Click on that link to see more comparisons.)

## Slide 10: Upgrade your RPIs
RPi = Raspberry Pi
We’re going to be busting out the touchscreens on Thursday, but the touchscreens don’t work until the RPIs have been fully upgraded (including the firmware).
Follow the directions on Blackboard, and we should be good to go.
Leave the username/password as pi/raspberry for now.

## Slide 11: Use VIM on RPI.csci4x.com
Ok, go ahead and log in on the server: rpi.csci4x.com
All text editing on the system must be done on VIM, so go ahead and learn that if you don’t know it yet.
I have temporarily enabled nano (i.e. pico), but I will be turning it off soon, so learn VIM.

## Slide 12: No more pico means...

## Slide 13: Buildchain for assembly
Suppose you’ve created an assembly program in test.s
  (Assembly files end in .s)
Assemble it by typing: as -o test.o test.s
Link it by typing: ld -o a.out test.o
I recommend making a Makefile to build your assembly projects for you, so you can just type “make” rather than doing this every time. I’ve given you a sample one.

## Slide 14: Compiler Assembly linker loader

## Slide 15: ARM32 ASSEMBLY - MOV
Let’s just jump into it and learn some commands:
The MOV (move) command loads a value into a register from another register or an immediate value.
  MOV r0, #42 @Sets r0 equal to 42
  MOV r9, r0 @Sets r1 equal to r0
The immediate number must always be on the right side.
There’s a bit more to it that we’ll learn later on.

## Slide 16: ARM32 ASSEMBLY - ADD
The ADD (which stands for “add”) command sets the value of the first register to the sum of the second and third.
ADD r0, r1, r2 @sets r0 = r1 + r2
ADD r8, r3, #42 @sets r8 = r3 + 42
Like with most commands, immediate values can only go into the second operand. (A “Flexible second operand”.)
  Wrinkle: The immediate value can be any 8 bit value, bit shifted.

## Slide 17: ARM32 ASSEMBLY - SUB
The SUB (“subtract”) command sets the value of the first register to the sum of the second and third.
ADD r0, r1, r2 @sets r0 = r1 - r2
ADD r8, r3, #42 @sets r8 = r3 - 42
Like with most commands, immediate values can only go into the second operand. (A “Flexible second operand”.)
  Wrinkle: The immediate value can be any 8 bit value, bit shifted.

## Slide 18: ARM32 ASSEMBLY – CMP
The CMP (“compare”) command is the first part of an if statement in ARM32 assembly. It sets a special flag to true depending on the result of the comparison.
CMP r9, r11 @Is r9 == r11?
BEQ some_label @If yes, jump to some_label
.... @All this code would get skipped
some_label: @...and start running from here...

## Slide 19: ARM32 ASSembly – B
A B (branch) instruction checks the status bits set by a CMP and jumps to a label. Suppose we did CMP r0,r1:
BEQ will jump to the label if r0 == r1
BNE will jump to the label if r0 != r1
BGE will jump to the label if r0 >= r1 (BLE is <=)
BGT will jump to the label if r0 > r1 (BLT is <)
BAL will always jump to the label. (Can just write B.)

## Slide 20: Branch statements and LABELS
Branch statements jump to the specified label, which are spots in your assembly code that you mark with a name followed by a colon. They’re useful for labelling spots in your code.
  CMP r0, #42 @Test to see if r0 is equal to 42
  BEQ foo @Branch if equal
  BNE bar @Branch if not equal. Will run if the BEQ doesn’t.
  foo: @A label. (Isn’t actually executable code.)
  ...do cool stuff...
  bar: @Another label, marking another line of code.
  ...do other cool stuff...

## Slide 21: Sample code
MOV r4,#16
MOV r5,#99
CMP r4,r5
BGT bar
BEQ baz
BAL foo
...lots of lines in between...
foo:
...turns on an LED light...
bar:
...turns off an LED light...
baz:
...Print “Hello World!”...

## Slide 22: Quitting a program
If you don’t explicitly exit your program back to the operating system, then your program will crash.
So at the end of every one of your programs you must put the following two lines:
MOV r7, #1 @This tells the OS to execute syscall 1
SWI 0 @This tells the OS to execute a syscall
Syscall 1 in UNIX is exit(), which just quits the program.

## Slide 23: EXIT STATUS
Every time you run a program in UNIX, it leaves an exit status behind for the operating system to detect.
Typically an exit status of 1 means an error occurred
  This is often used in shell scripts to detect a crashing server, which can then be used to restart the server.
An exit status of 0 means the program terminated normally
  If the user deliberately quit, you don’t want to restart it.

## Slide 24: EXIT STATUS
For now, since we don’t know how to print stuff out in assembly yet, we’ll use the exit status to output numbers.
The exit status is whatever value is in r0 at the end of the program.
So MOV r0, #6 before quit will leave an exit status of 6
From the UNIX prompt, we can echo the exit status by:
  echo $? (will print 6)

## Slide 25: Sample Code
Check your ~/assembly_example code on the server
It holds example code for everything done today.
Try changing some of the values and see that the BGT, BLT, etc., branches function as you think they should.
Remember the steps to build, run and test your code:
  make
  a.out
  echo $?

## Slide 26: Homework 2.0
Convert your programs from Homework 1 to ARM assembly (you know all the needed ARM commands now). Start off by setting r0 and r1 to whatever values you want to multiply or modulus or whatever.
Run them on the server to make sure they work.
They will not be autograded, but you sure test them there.
Print them out on paper and hand them to me next class.