## Slide 1: CSCI 45 – Avengers Assemble
Professor Kerney

## Slide 2: Comparisons and The Status register
The status register ONLY gets set by a CMP operation
  This includes the S (set) suffix which does a free CMP for you.
The status register bits that get set by CMP are:
  Zero: If the number == 0
  Negative: If the number < 0
  Carry: If we carried an extra bit out of an addition operation
  Overflow: If we multiplied two numbers and the result was too big

## Slide 3: Comparisons and The Status register
All of these bits remain set until the next time you do a CMP (or –S suffix)
They get used via the condition suffixes (which work with anything):
  BGT Branch if Greater Than
  BCS Branch if Carry bit is Set
  BCC Branch if Carry bit is Clear
  SUBLE SUBtract if Less Than or Equal
  MOVVS MOVe if oVerflow bit is Set.

## Slide 4: The basics will get you most places
Arithmetic: Add (ADD), Multiply (MUL), Subtract (SUB).
Move (MOV)
Compare (CMP)
Branch (B)
Suffixes:
  S: Can be added to the end of any command to do a free Compare (CMP).
  GT, GE, LT, LE to the end of any command to run it conditionally.

## Slide 5: Weird commands are people too
So there’s some alternate commands for special needs
MLA: Multiply with Accumulate. Remember how we said assembly could offer commands C++ could not? This is a major one of those, a multiply and add.
  Example: r0, r1, r2, r3 //r0 = (r1 * r2) + r3
RSB: Reverse subtract. Because only the second operand is flexible, RSB exists which basically swaps the first and second operands then does a SUB.
  Example: RSN r0, r1, #222 //r0 = 222 – r1

## Slide 6: Functions
I realized how hard it was to have you guys write Fizzbuzz without real functions, so I semi-kinda introduced them, but I’ll explain it more now.
Basically a function in the C sense is a reusable block of code, that (optionally) takes some parameters, and (optionally) returns a value.
In assembly, it’s a label that (optionally) takes some parameters and (optionally) returns a value.
For C interoperability, a function and a .global label are the same thing!

## Slide 7: Functions
There’s certain rules that ALL code obeys, so that everyone plays nicely with each other, and you can call to and from C code without any issues.
These rules are called the “ABI” – Application Binary Interface:
  Parameters to the function are passed in via R0-R3. (What if you have more than 4?)
  Call the function using the BL command. (Like “BL print_fizz”)
  The function preserves registers R4-R12 from being corrupted.
  The return value from the function is returned via R0.

## Slide 8: Functions Step 1 – Pass in parameters
If you want to pass in up to four parameters, it’s pretty easy, just set R0 through R3 to what you want the parameters to be.
With C functions, it looks like print_number() takes R1 as the first parameter instead of R0, so you might need to experiment a bit to see which parameter is which. Always test your code!
With “int tester(int a, int b, int c, int d)”, though, it indeed is R0 through R4.
If you want to pass in more than 4 params, you need to use the stack.

## Slide 9: Functions Step 2 – Call the function
The ARM assembly language has limited support for functions.
The BL (Branch with Link) command is the one bit of support it has.
  All it does is save the place you’re at into R14, and then do a normal branch.
  This lets the function return to back where you are (well, the next command I guess)
  And this is why you shouldn’t use R14 like a normal register in a function.
So if you want to call a function in ARM ASM or C, you just do something like:
  BL print_fizz

## Slide 10: Functions STep 3 – Preserve old registers
Most functions need more than R0-R3 to run, but they’re not allowed to corrupt the values in R4-R12. (Or R14, as we saw on a previous slide.) So…?
You need to save the old registers to the “stack”.
The stack pointer is held in R13. You… can… use it manually, but no.
Use the PUSH command to save values onto the stack
Use the POP command to restore them to their previous values

## Slide 11: Functions STep 3 – Preserve old registers
So basically every function you write should begin like this:
PUSH {LR} //This saves R14 from being corrupted
PUSH {R4-R12} //This saves R4 through R12 from being corrupted
And every function should end like this:
POP {R4-R12} //Restore the original values of R4 through R12
POP {PC} //Set the PC equal to the original LR… RETURN!

## Slide 12: Functions STep 4 – Run your code
Now that you’ve been passed in some parameters and you’ve preserved R4-R12, you are free to change them as much as you like (since they’ll be restored later to their original values).
So run your code, go wild, be free, etc. etc.
When you’re ready for your code to return, you write the result into R0.
Example: MOV R0, #99
Then you do the two POP statements, which restores the registers and returns.

## Slide 13: The Application Binary Interface
This ABI thing is basically a mutually agreed upon thing so that every programmer’s code will work with every other programmer’s code. Each platform has its own.
All library functions, C code, professional assembly functions, etc., will ALL follow the ABI. This allows code to be combined into larger systems, which is critical.
HOWEVER, they are really more guidelines than a rule. If your code is only calling your own code, you can gain a performance boost by not saving all 9 registers (R4 through R12) to memory, which is very costly, if you don’t need to.
  Cheating is a main advantage ASM has over C. C compilers have to play by the rules.
Also, functions that don’t call any functions (“leaf” functions) can cheat a little bit also.

## Slide 14: example “Add4” function
.global add4 //Allow this to be called by C
add4: PUSH {LR} //Preserve LR
PUSH {R4-R12} //Preserve registers
ADD R5,R0,R1 //R5 = R0 + R1
ADD R6,R2,R3 //R6 = R2 + R3
ADD R0,R5,R6 //R0 = R5 + R6. Return value.
POP {R4-R12} //Restore registers
POP {PC} //Return to the calling function

## Slide 15: Calling Add4 from C
From C:
  extern int add4(int a, int b, int c, int d);
  …and then below…
  int x = (1,2,3,4); //Will set x equal to 10
The extern keyword actually is optional here, but it’s a clue for people reading the code that the function is written in another language.
  If you want to call C or ASM code from C++, it is required: extern "C" add4(…);

## Slide 16: Calling add4 from ASM
MOV R0,#3 //Parameter 1
MOV R1,#6 //2
MOV R2,#9 //3
MOV R3,#12 //4
BL add4 //Call the function
MOV R5,R0 //R5 = R0+R1+R2+R3